## Slide 1: Turkey Innovative Approach to Combustion Byproducts
SBB Energy – ABH

## Slide 2
Introduction
Innovative magnesium FGD vs standard calcium FGD
Combustion Byproducts - application as fertilizer
Kangal Tirmik - case study
Summary
Agenda

## Slide 3
Introduction
Innovative magnesium FGD vs standard calcium FGD
Combustion Byproducts - application as fertilizer
Kangal Tirmik - case study
Summary
Agenda

## Slide 4
Introduction
Innovative magnesium FGD vs standard calcium FGD
Combustion Byproducts - application as fertilizer
Kangal Tirmik - case study
Summary
Agenda

## Slide 5
by-product
sorbent
General concept and chemical mechanisms are similar for calcium and magnesium based wet FGD systems.
For both systems sorbent is mixed with water and sprayed in absorbtion tower to wash flue gas and absorb SO2.
What is the difference?
Key difference is the product of chemical reaction.
Innovative magnesium FGD vs standard calcium FGD
Source: Wikipedia

## Slide 6
Absorption unit
Filtration unit
Adiabatic evaporation
unit
Crystallization unit
Drying unit
Storage silo
Magnesium based wet FGD concept

## Slide 7
Innovative magnesium FGD vs standard calcium FGD
 | Synthetic Gypsum | Magnesium Sulphate
Form | Non-soluble solid, white powder | Easily soluble white or colorless crystals
Usage in Turkey | Non | Agriculture, chemistry, cosmetics, pharmacy
Market price | $0/t | $150-210/t
Source: https://www.alibaba.com/product-detail/synthetic-gypsum_50029556258.html
Source: http://www.matuta.de/chemicals-for-balling/Magnesium-sulfate-heptahydrate.html

## Slide 8
Introduction
Innovative magnesium FGD vs standard calcium FGD
Combustion byproduct - application as fertilizer
Kangal Tirmik - case study
Summary
Agenda

## Slide 9
Source: https://extension.umn.edu/micro-and-secondary-macronutrients/
magnesium-crop-production
Magnesium is a key element of chlorophyll molecule in plant tissue. Thus, if Mg is deficient, the shortage of chlorophyll results in poor and stunted plant growth.
In agriculture, magnesium sulfate is used to increase magnesium or sulfur content in soil. It is most commonly applied to potted plants, or to magnesium-hungry crops. The advantage of magnesium sulfate over other magnesium soil amendments is its high solubility, which also allows the option of foliar feeding. Solutions of magnesium sulfate are also nearly pH neutral therefore, the use of magnesium sulfate as a magnesium source for soil does not significantly change the soil pH.
Magnesium in agriculture

## Slide 10
Magnesium fertilizer market
Source: Maia Research Analysis
Global Magnesium Sulphate has very broad market in 21st century and it has been evaluated as $755.72 MM. Countries located in APAC region like India, China and Japan where healthcare and agriculture sector together contributes more than 40% of total GDP. The value of Magnesium Sulphate markets is expected to be $1071.42 MM by 2025.
In Magnesium Sulphate market, the Agricultural holds an important share in terms of applications and main recipients.
The global production of ready - made mineral fertilizers in 2018 amounted to almost 4.1 million Mg and was nearly 32.5% higher compared to 2014.
Nowadays, Asia-Pacific region is recognized as one of the major markets for Magnesium Sulphate Fertilizers, with India playing main role.

## Slide 11
Magnesium fertilizer market
Chart: 
| Total | Pharmaceutical | Others | Livestock | Industrial | Agricultural
2019 | 4378.1 | 821.2 | 161.8 | 242 | 906 | 2247.1
2025 | 6893.2 | 1323.5 | 247.5 | 357.8 | 1457.2 | 3507.3
Fig. Table Global Magnesium Sulphate Consumption Growth Rate by Application (2019- 2025) (K Tons)
(Source: Maia Research Analysis)
CAGR (2019-2025) 7.70%
CAGR (2019-2025) 6.73%
CAGR (2019-2025) 8.24%
CAGR (2019-2025) 8.28%
CAGR (2019-2025) 7.34%
CAGR (2019-2025) 7.86%

## Slide 12
Magnesium fertilizer market
Source: Global Magnesium Sulphate Market Insights, Forecast to 2025.
Asia-Pacific is one of the major markets, wherein India is expected to be the potential agricultural economy in the coming years.
Chart: Consumption for Agricultural Application in 2019
| North America | Europe | Asia Pacific | Central & South America | Middle East & Africa
2019 | 1033.2 | 1149.3 | 1683.8 | 254.2 | 257.7
2025 | 1586.1 | 1764 | 2711.8 | 421.9 | 409.5
 | 153.5134 | 153.4847 | 161.0524 | 165.9717 | 158.9057

## Slide 13
Magnesium fertilizer market
Based on Global Magnesium Sulphate Market Insights, Forecast to 2025.
Since 2014, there has been an increase in the production of magnesium sulfate, which is a consequence of the rapidly growing demand for fertilizers in developing countries, in particular in China, India and Brazil.
North America 35,4 %
Central &
South America 50,2 %
Middle East
and Africa 43,2 %
Europe 40,5 %
Asia Pacific 46,4 %
consumption increase on the map in %

## Slide 14
Introduction
Innovative magnesium FGD vs standard calcium FGD
Combustion Byproducts - application as fertilizer
Kangal Termik Santrali - case study
Summary
Agenda

## Slide 16
Kangal Termik Santrali

## Slide 17
Kangal Power Plant general characteristics
 | UNIT 1 | UNIT 2 | UNIT 3
Commissioned | 1989 | 1990 | 2000
Power [MW] | 150 | 150 | 157
Flue gas flow (dry) [Nm3/h] | 860,000 | 860,000 | 860,000
SO2 (dry, 6% O2), max [mg/Nm3] | 12,500 |  | 
Average annual operation time [h] | 7, 500 | 7,800 | 7,700

## Slide 18
Kangal Power Plant general characteristics
Absorbtion unit 3
Absorbtion unit 1 & 2
Filtration, Crystalization, Drying
Packing warehouses
Mixture concentration

## Slide 19
Emission reduction results
 | Current emission | Anticipated emission | Emission reduction | Emission reduction
Emission level [mg/Nm3] | 12 500 | 200 | 12 300 | 98.4%
SO2 emission [kg/MWh] | 70.6 | 1.1 | 69.5 | 

## Slide 20
Kangal Power Plant general characteristics
Magnesium FGD
Higher CAPEX
OPEX costs of magnesium method are positively covered by fertilizer sale.
Calcium wet FGD
Lower CAPEX
Constant deliveries of limestone create high OPEX without possibility to sell byproducts.

## Slide 21
Kangal Power Plant general characteristics
Overall cashflow of the project is positive only in Magnesium method

## Slide 22
Introduction
Innovative magnesium FGD vs standard calcium FGD
Combustion Byproducts - application as fertilizer
Kangal Tirmik - case study
Summary
Agenda

## Slide 23
Summary
The largest of a kind
The first in Turkey
High efficiency of flue gas cleaning
Lower water consumption
Valuable byproduct
Great positive impact on environment

## Slide 24
Thank you for your attention!